## Slide 1: IETF Hackathon: Measurements that Lead/Follow Stds: Three Projects
IETF 103
3-4 November, 2018
Bangkok

## Slide 2: QUIC Delay Sample
Subject: Measuring accurate RTT over QUIC protocol (with visibility from an intermediate observer).
Reference: draft-trammell-quic-spin-03
Goal: to reduce from 3 to 2 bits the header space used for delay measurements (VEC proposal)
Job: implementing the Delay Sample (DS): Spin Bit+DS bit
Experimentation: Comparison between Delay Sample and Valid Edge Counter (VEC):
    Pros 1 bit saving
      Better measurements in case of out of order
    Cons less measurements in case of «traffic holes» and losses (1 empty period more)
    Observer implementation (needs a timer to clean edges)
Web site: http://5.135.192.128/

## Slide 3: Benchmarking & IP Access Measurement Cross-over
Access moving to Gbps & Low Latency
Benchmark Methods: UDP & new Robust Search alg.
Today’s Access Test Methods: N x TCP conn.
Test using Calibrated DUT
Results: UDP found Cap Limits! Best perf using MTU
Need to get iPerf working, etc.
Test Device
(Send&Rcv)
Netem Traffic Control on Egress, multiple shaper traffic filters
vSwitch
Physical
port
Physical
port
Multiple SW-based Traffic Generators and Measurement systems
Access Capacity
(xxxx Mbps)
or

## Slide 5: Wrap Up
Team members:
Mauro Cociglio*, Fabio Bulgarella*
Thomas Fossati
Al Morton
* First timers @ IETF/Hackathon
Web site: http://5.135.192.128/
https://github.com/thomas-fossati/llt
See OPNFV Wiki
https://wiki.opnfv.org/display/vsperf