## Slide 1: IETF Hackathon: DOTS Interop
IETF 103
3-4 November, 2018
Bangkok

## Slide 2: Hackathon Plan
DOTS: DDoS Open Threat Signaling
  standardization of signaling for DDoS protection
  The core specification of DOTS protocol is submitted to IESG for Publication now
Problem: To show DOTS protocol’s functional superiority of DDoS protection.
How you planned to solve it? -> OK, let’s do DDoS Attack

## Slide 3: What got done
overwhlemed link by SYN flood
  over 90% packet loss for downstream
  no packet loss for upstream
2 independent implementations and different mitigation capability
  ACL, BGP handling
  Inline Security Appliance
See if they can protect the property
Internet
Router
DOTS
Server
Narrow Link
(1Mbps)
DOTS
Client
DDoS Attack
(overwhelm
the narrow link)
Web Servers
Router
Router
mitigation
DOTS
Protocol

## Slide 4: What we learned
Mitigation requests work even under the hostile network situation by design
Issues found:
  supportive function doesn’t work under attack
    heartbeat mechanism
    reconnection of DTLS
    install of filtering rules
  A lot of Implementation considerations
Will be reported to WG
trigger mitigation | OK
CoAP ping: | NG -> retry happens
DTLS handshake | NG
DataChannel | NG
Communication Under Hostile Situation
Signal Channel Layers
IP
TCP
UDP
TLS
DTLS
CoAP
DOTS
Data Channel Layers
IP
TCP
TLS
RESTCONF
DOTS

## Slide 5: Wrap Up
Team members: Kaname Nishizuka (NTTCom)
Nagata Takahiko (Lepidum)
Jon Shallow (NCC Group)
Liang 'Frank' Xia (Huawei)
First timers @ IETF/Hackathon:
Thank You!