## Slide 1: IETF Hackathon: TCP Authentication Option (TCP-AO)
IETF 103
3-4 November, 2018
Bangkok

## Slide 2: Hackathon Plan
Provide better support of TCP-AO on Linux, as a reference implementation
  RFC 5925, RFC 5926
  TCP-AO replaces RFC 2385 (TCP-MD5), which is no longer considered safe to use, but remains in practice due to a lack of TCP-AO implementations
Activities
  Start a kernel implementation of the TCP option
  Provide full support of the TCP option in tcpdump(1)
  If multiple existing router implementations became available, do some basic interop testing

## Slide 3: What got done
We did start the kernel implementation
  Sorted out how the application adds/deletes keys with setsockopt(3), defined some data structures, and began the kernel coding/testing.
  Initial commits in
    https://github.com/vlolteanu/linux-tcp-ao (kernel)
    https://github.com/vlolteanu/tcp-ao-user (app header file)
We did start working on the tcpdump(1) implementation, including being able to enter the TCP-AO master key to verify that the option is properly formatted

## Slide 4: What we learned
TCP-AO is quite a complex for a TCP option, even compared to TCP-M5
  Generating traffic keys from a master key is better security, but requires a significant amount of state to be maintained in the kernel
  Allowing multiple master keys per session is required for key rollover, but having the strict ordering of “current, next” keys makes for a more complicated state machine (especially if more than 2 master keys have been added for the socket)
  Some implementation guidance is going to be necessary, but we aren’t far enough to provide that yet.

## Slide 5: Wrap Up
Team members:
Vladimir Olteanu
Tero Kivinen
Brian Weis
First timers @ IETF/Hackathon:
Vladimir Olteanu